## Slide 1: Adaptive Multi-Hazard Early Warning and Evacuation Support System
Global by design · First deployment: Nepal
Requirements Engineering · 4-week MVP with live data + launch roadmap
AMHEWS
Normal
Watch
Warning
Critical
Semester MVP — decision support. Public warnings and sirens need authorization by the government authorities.
Notes: Introduce the project: a globally deployable, requirements-engineering-led design for flood early warning and evacuation support, piloted first in Nepal. Stress that it is decision support, not disaster prevention.

## Slide 2: What this presentation covers
1 Project & context
Problem, global scope, Nepal pilot, research questions, objectives
2 Stakeholders
24 stakeholder groups, needs, goal model, personas
3 System design
Context, architecture, live data & hardware, risk levels, lifecycle, data, API
4 Requirements
75 functional, 42 non-functional, safety, security, privacy
5 Analysis
Use cases, user stories, 20 failure scenarios, conflicts, adaptivity
6 Process & plan
RE lifecycle, 4-week plan, launch roadmap, traceability, V&V, ethics
Notes: Six parts. The full detail is in REQUIREMENTS_ENGINEERING.md and the docs folder in the repository.

## Slide 3: What the system is — and what it is not
It is
Global decision support — any country, via a profile
Early warning: monitors data and assesses risk per area
Localized, multilingual, actionable alerts
Shelter and safe-route guidance for evacuation
Keeps working when data or networks fail
It is not
A way to prevent floods
A guaranteed prediction or a guarantee of safety
A replacement for national or local authorities
An autonomous siren trigger or dam controller
Live for the public before government sign-off
Objective: reduce casualties, injuries, evacuation delays and misinformation through earlier, clearer and better-targeted information and coordination.
Notes: This framing is a requirement in itself (SR-10): every screen states the system is decision support.

## Slide 4: Global by design — Nepal is the first pilot
One product, any country
Everything that differs between places comes from a Deployment Profile (FR-68). Nothing country-specific is hard-coded.
Nepal is the testing ground: monsoon floods, mountains, landslides, uneven connectivity and many languages. If it works there, it should transfer.
Concern | Global product | Nepal pilot profile
Administrative levels | Configurable hierarchy | Province → district → municipality → ward
Hydromet authority | Role, set per country | DHM
National DRR authority | Role, set per country | NDRRMA (BIPAD)
Languages | Any language pack + English | Nepali + English
Time zone, calendar | Any time zone; local calendar | UTC+05:45; Bikram Sambat
Laws, emergency numbers | Per profile | Nepal privacy & DRRM law
Data sources | Adapters; global APIs | Simulated Terai river gauges
Channels | Push, SMS, siren, broadcast | Web push + simulated SMS
Notes: Key framing: the system is not built for Nepal only. Nepal is the first pilot deployment and testing ground. A second test profile proves the global claim.

## Slide 5: Why Nepal is the first pilot: a demanding test case
753
local levels (460 rural municipalities) and 6,743 wards
[F] MoFAGA / Open Data Nepal
124
mother tongues recorded in the 2021 census
[F] NSO census 2021
44.86 %
speak Nepali as mother tongue — over half do not
[F] NSO census 2021
Jun–Sep
monsoon brings most annual rainfall and most floods
[F] DHM climate data
Late-September 2024: monsoon floods and landslides killed at least 148 people (reported 29 Sept) and blocked highways out of Kathmandu [F, AP/NPR; final toll per NDRRMA higher].
What the pilot tests [D]
SMS-first for WARNING+
Nepali + English + icons
Ward-level targeting
Offline-capable app
Volunteers & sirens in loop
Notes: Tags: [F] verified fact, [A] assumption, [D] design decision, [T] prototype target. Facts are listed with sources in docs/07.

## Slide 6: Problem statement and core research question
People at risk can receive warnings that are…
Late
Warnings arrive after water is already rising
Too general
District-wide alerts, not ward-specific
Not understood
Language, literacy, disability, jargon
Not received
Weak networks, no smartphone, no power
…while authorities decide under time pressure from fragmented data of uneven reliability [A].
CORE RESEARCH QUESTION
How can an adaptive, globally deployable early warning and evacuation support system reduce the human impact of floods by providing timely, reliable, localized and actionable risk information — evaluated first in a Nepal pilot?
The RE problem: what must the system do, how well, and under which failures — and how do we show the requirements are complete, consistent, traceable and validated?
Notes: This is not framed as an ML prediction problem; the academic focus is requirements under uncertainty.

## Slide 7: Supporting research questions
RQ | Theme and question
RQ1 | Early detection — which data signals give useful lead time?
RQ2 | Risk assessment — how to keep risk explainable and configurable?
RQ3 | Warning generation — which rules prevent contradiction and loss?
RQ4 | Communication — which channels and formats are understood?
RQ5 | Evacuation — how to never recommend unsafe routes or shelters?
RQ6 | Accessibility — what serves disabled, elderly, low-literacy users?
RQ7 | Reliability — what availability is proportionate for a prototype?
RQ | Theme and question
RQ8 | False alarms — how to balance missed warnings against fatigue?
RQ9 | System failures — which failures, detected and mitigated how?
RQ10 | Conflicts — which stakeholder conflicts, resolved by which RE techniques?
RQ11 | Limited infrastructure — how to degrade gracefully?
RQ12 | Safety — which requirements are safety-critical, verified how?
RQ13 | Privacy & security — alerting with minimal data and no spoofing?
RQ14 | Validation — how to validate with hard-to-reach stakeholders?
Notes: Each RQ maps to a section of the specification; e.g. RQ5 to FR-38..46 and SR-03/05.

## Slide 8: Measurable system objectives
Early detection
Risk updated ≤ 60 s after new data [T]
Four clear levels
100 % match with scenario oracles
Localized alerts
0 alerts delivered outside target area
Actionable
≥ 80 % of test users pick the right action [T]
Safe routes
0 routes through hazard zones or closures
Any language
100 % of strings in every configured language (pilot: Nepali + English)
Works offline
Last risk, shelters, instructions cached
Accountable
100 % of warning actions in audit log
Notes: Targets marked [T] are prototype acceptance targets measured in a simulated environment, not real-world guarantees. Full list SO-1..SO-16 in docs/01.

## Slide 9: Semester scope: live data, real hardware pilot
In scope (semester MVP)
Live satellite rain & flood data (GPM, Sentinel-1, GloFAS)
1–3 own IoT river gauges at one pilot site
1 siren controller pilot — human-authorized, test mode
DHM station adapter (live after data agreement)
Rule-based risk engine with confidence
Warning workflow with human approval
Citizen app, authority dashboard, admin
Shelters, safe routing, audit log, degraded mode
Not this semester
Own country-wide sensor network (use DHM's)
Autonomous sirens or warnings without approval
Control of dams or any infrastructure
Replacing government warning authority
Guaranteed prediction or safety
Cell broadcast (needs telecom / NTA agreement)
Public alerts before government sign-off
24/7 national operations (roadmap Phase 3)
Notes: Scope is deliberately constrained so a 4-person team can deliver in 4 weeks while still demonstrating every safety requirement.

## Slide 10: 24 stakeholder groups in five classes
At-risk public
Residents, flood-prone households, farmers, elderly, children, persons with disabilities, tourists
Authorities
Local, district and national DRR authorities (pilot: wards, municipalities, NDRRMA)
Responders
Police, armed police, army, fire services, hospitals, search-and-rescue teams
Partners & providers
NGOs / Red Cross, volunteers, telecoms and regulator, hydromet service, road authorities, data providers
Builders
System administrators, software developers
Each analysed on six dimensions: goals · responsibilities · information needs · concerns · constraints · conflicts with others
Notes: Full stakeholder tables in docs/02 §3.

## Slide 11: Power–interest grid and engagement
Keep satisfied
Telecoms and regulator, army, road authorities
Manage closely
National DRR and hydromet authorities, local and district government, police, system admins
Monitor
Tourists, external data providers
Keep informed
NGOs, volunteers, hospitals — and at-risk residents ↑
Power →
Interest →
Ethical override [D]
At-risk residents have little formal power but the highest stake: their lives. They are treated as “manage closely” for elicitation and validation — interviews, questionnaires and usability tests focus on them.
Notes: Engagement plan follows the grid; residents are elevated by an explicit ethical decision.

## Slide 12: Stakeholder needs (StRS level)
ID | Need | Who
STK-01 | Know early when my area may flood | Residents
STK-02 | Understand it in my language and ability | Residents, PwD
STK-03 | Get warnings without smartphone or data | Feature-phone users
STK-04 | Know where to go and how, safely | Residents
STK-05 | Report what I see; ask for help | Residents, volunteers
STK-06 | Trustworthy risk picture per jurisdiction | Authorities
STK-07 | Final say over high-impact warnings | Authorities
STK-08 | One voice; never contradict official | Hydromet, DRR
ID | Need | Who
STK-09 | Know if warnings reached people | Authorities, SAR
STK-10 | Current shelter and road information | Shelter mgrs, police
STK-11 | Personal data not misused | Citizens, NGOs
STK-12 | No fake warnings possible | All
STK-13 | Configure areas without developers | Admins
STK-14 | Add hazards without redesign | DRR auth., devs
STK-15 | Keep working when infrastructure fails | All
STK-16 | Evidence to learn after each event | DRR, hydromet
Notes: Each STK need is refined into system requirements; the mapping is in REQUIREMENTS_ENGINEERING.md §3.

## Slide 13: Goal model: from impact to requirements
G0 Reduce human impact of floods
G1
Know the risk early
FR-01–10
G2
Assess risk per area
FR-11–17
G3
Warn the right people
FR-18–37
G4
Enable safe action
FR-38–46
G5
Coordinate authorities
FR-51–58
G6
Survive failures
FR-47–50
G7
Trust & accountability
SEC, PRV, FR-59
G8
Adapt to new contexts
FR-63–67
Obstacles (anti-goals): missed warning, false warning, delayed warning, spoofed warning, unsafe route, full shelter, misunderstanding, fatigue — each analysed as a failure scenario and mitigated by a requirement or assigned to a human agent.
Notes: KAOS-style refinement. G3 is refined further into G3.1 no contradiction/loss, G3.2 human authority, G3.3 understandable by all.

## Slide 14: Pilot personas (Nepal) guide the requirements
Sita Tharu, 38
Rice farmer, Bardiya (Terai)
Shared Android phone, little data, reads Nepali slowly; mother-in-law with limited mobility, two buffaloes.
Needs early Nepali SMS, a shelter that takes livestock.
FR-35 · FR-39
Ram Bahadur Karki, 74
Retired teacher, lives alone
Feature phone, hard of hearing; son works abroad.
Needs simple SMS, son subscribes for him, help to leave.
FR-32 · FR-36
Anjali Shrestha, 29
Ward disaster focal person
Not an IT specialist; on call in monsoon; fears a wrong evacuation order.
Needs evidence, recipient preview, safe cancel, audit trail.
FR-20 · FR-53
Emma Müller, 31
Foreign trekker, Western Nepal
No Nepali, no local SIM, Wi-Fi at guesthouses.
Needs English alerts via QR area code and clear icons.
FR-34 · NFR-U4
Composite, fictional personas [A] — four more (volunteer, police officer, admin, wheelchair user) in docs/02; all to be validated in interviews.
Notes: Personas make abstract stakeholder classes concrete and drive acceptance criteria.

## Slide 15: System context and boundary
Data: satellites (GPM, Sentinel-1, GloFAS) · DHM stations · own IoT gauges · weather · OSM · population · reports
AMHEWS
ingest → validate → assess → propose → approve → disseminate → log
+ shelters and safe routing
Citizens, volunteers, tourists
risk, guidance ↔ reports
Authorities & responders
approve, issue ↔ situation
Channels
web push · SMS · email · sirens (authorized only)
Other systems
National alert systems via CAP (pilot: BIPAD)
Administrators — configure & monitor
Inside the boundary: validation, risk, warning workflow, messages, dissemination, guidance, logs. Outside: sensors, networks, legal authority to order evacuation.
Notes: Boundary decision [D]: the system never owns gauges, sirens, telecom networks or legal authority.

## Slide 16: High-level architecture: a modular monolith
Presentation
Next.js PWA
Citizen PWA
Authority dashboard
Admin console
Application
FastAPI
Ingestion: API, MQTT, satellite
Validation & quality
Risk engine
Flood plug-in
Warning manager
Notification dispatcher
Evacuation routing
Shelter management
Audit logger
Device & health monitor
Data
Supabase
PostgreSQL + PostGIS
Auth + RLS
Realtime
Storage
REST + Supabase Realtime between layers · one deployable backend with clean module interfaces (can be split later) · hazards added as plug-ins (HazardModel)
Notes: Why not microservices: disproportionate deployment and failure-mode complexity for a 4-week, 4-person team. Revisit at national scale.

## Slide 17: Technology stack
Database
Supabase Postgres + PostGIS
Spatial queries, RLS, realtime, auth
Backend
FastAPI · Pydantic · APScheduler
Typed API, scheduled data checks
Routing
OSMnx + NetworkX
Remove flooded roads before path search
Frontend
Next.js 15 · TypeScript · Tailwind · shadcn/ui
Fast, accessible UI
Maps & language
MapLibre GL · OSM tiles · next-intl
Risk layers; any language
Offline & alerts
Serwist PWA · Web Push · SMS simulator
Works offline; channel-swappable
IoT: ESP32, MQTT (Mosquitto / EMQX) · Testing: pytest, Playwright, k6 · Hosting: Vercel, Render / Fly.io, Supabase
Notes: Avoided in 4 weeks: microservices, ML forecasting core, native apps, own country-wide sensor network.

## Slide 18: Live data sources and field hardware
Satellite (country-wide, free)
NASA GPM IMERG rainfall every 30 min (a few hours' delay) · Copernicus Sentinel-1 radar flood extent, every few days, sees through cloud · GloFAS river forecasts
Government station network
DHM hydrological and rainfall stations across Nepal · adapter built this semester; live after a data-sharing agreement [A]
Own river-gauge node (1–3)
ESP32 + ultrasonic or radar level sensor + rain gauge · solar + battery · GSM / LTE or LoRa · MQTT over TLS · 24 h offline buffer
Siren node (1 pilot)
GSM relay controller · signed commands only from approved warnings · local manual button · heartbeat and weekly silent self-test
Field failures: silent node → device fault, level held (SR-06) · siren offline → operators and volunteers alerted · tampering → readings marked SUSPECT
Notes: Satellites give rainfall and flood extent, not real-time river levels; gauges give river levels. Country-wide gauge input comes from DHM's existing network, not from building our own network.

## Slide 19: Risk levels and transparent classification rules
NORMAL
No elevated risk detected
Stay informed
No alert
WATCH
Flooding possible
Prepare: charge phone, pack go-bag, know shelter
Auto (policy) or 1 approver
WARNING
Flooding likely
Move valuables, livestock, vulnerable people
1 approver
CRITICAL
Flooding now or imminent
Evacuate now; never cross flowing water
2 approvers; cannot be muted
UNKNOWN
Not enough valid data
Follow local authorities
Operators alerted
Flood rules (all thresholds configurable): R1–R3 level vs watch / warning / danger · R4 fast rise +1 level · R5 upstream station lead · R6 24-h rainfall · R7 forecast alone ≤ WATCH · R8 missing data holds level, confidence LOW · R9 final = highest rule · R10 lower only after hold time
Notes: Rules rather than ML: explainable, verifiable with test oracles, feasible in 4 weeks. Thresholds in the prototype are illustrative; real ones come from DHM.

## Slide 20: Warning lifecycle: human authority built in
Rules or manual draft
PROPOSED
ACTIVE
SUPERSEDED
REJECTED
CANCELLED
EXPIRED
level ≥ WATCH
approve: 1 (WARNING) or 2 distinct (CRITICAL)
escalate or update = new version
reject + reason
cancel + reason → all-clear to everyone
valid-until passed
CRITICAL not decided in time → escalate to district; labelled precautionary publication if region policy allows
Invariants enforced in code and database
INV-1 at most one ACTIVE warning per area and hazard (partial unique index) · INV-2 every transition audited with actor, time, reason · INV-3 cancellation always sends a correction to the same recipients · INV-4 never below an official warning
Notes: This state machine realises FR-18..29 and SR-02, SR-07, SR-09.

## Slide 21: Data model: 14 core entities (Supabase + PostGIS)
Region / Area
names ne/en, hierarchy, polygon, population, vulnerability
Station / Device
type, location, heartbeat, battery, firmware
Threshold
watch / warning / danger, rise rate, version, approver
Observation
value, unit, observed / received time, quality, raw
Quality event
missing, stale, spike, flatline, conflict
Risk assessment
level, confidence, reasons, inputs, valid until
Warning
version, areas, level, status, approvers, messages
Subscription
areas, language, channels, consent, expiry
Delivery
channel, status, attempts, error, ack
Shelter
capacity, occupancy, status, accessible, livestock
Closure / Hazard zone
line or polygon, reason, source, validity
Report / Incident
category, location, depth, photo, status
Audit log
actor, action, entity, payload, hash chain
Profile / Role
role, area scope, MFA required
Data quality rules: quality flag on every reading · valid geometries · watch < warning < danger · every area monitored or flagged “no monitoring” · stale shelter occupancy shown as outdated
Notes: Full schema with RLS policies in docs/03 §4. Retention: reports 90 days, subscriptions 12 months, audit ≥ 5 years pseudonymised [D].

## Slide 22: External interfaces and API (REST, /api/v1)
Endpoint / interface | Access | Requirements
GET /areas/{id}/risk · GET /risk/map | Public | FR-13, FR-14, FR-31
GET /warnings/active?area= ¦ ?lat=&lon= | Public | FR-30, FR-31
POST /subscriptions · DELETE /subscriptions/{token} | Public | FR-32, PRV-06
GET /shelters/nearest · POST /evacuation/route | Public | FR-38–FR-44
POST /reports | Public, rate-limited | FR-37, SEC-06
POST /warnings · /{id}/approve ¦ reject ¦ cancel ¦ escalate | Operator, scoped, MFA | FR-20–FR-25
GET /warnings/{id}/recipients/preview · /deliveries/stats | Operator | FR-53, FR-57
PATCH /shelters/{id} · POST /road-closures · PATCH /reports/{id} | Operator / shelter mgr | FR-43, FR-55, FR-56
/admin/* (regions, stations, thresholds, templates, users) | Admin | FR-63–FR-68
GET /health · GET /status | Public | FR-48
Realtime: risk, warnings, shelters, system status | Dashboard | NFR-PF5
Channel adapter: send(message, recipient) → result | Internal | NFR-I3
MQTT devices/{id}/readings · devices/{id}/heartbeat | Device (own key) | FR-69, FR-70
POST /sirens/{id}/activate (approved warning only) | System, signed | FR-74, SR-13
OpenAPI 3 generated · errors as RFC 9457 problem+json · timestamps UTC (shown in local time; pilot UTC+05:45) · geometry GeoJSON WGS84 · CAP 1.2 export (Could)
Notes: The API contract is frozen in week 1 so frontend and backend can work in parallel.

## Slide 23: Requirements at a glance
Chart: Functional requirements by module and priority
| Data | Risk | Warning | Citizen | Evacuation | Offline | Dashboard | Logging | Admin | Devices & satellite
Must | 8 | 5 | 8 | 5 | 6 | 2 | 6 | 1 | 6 | 4
Should | 1 | 1 | 4 | 3 | 3 | 2 | 1 | 2 | 0 | 3
Could | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
75
Functional (FR)
42
Non-functional
14
Safety (SR)
10
Security (SEC)
8
Privacy (PRV)
16
Stakeholder needs
4-week split: 51 Must · 20 Should · 4 Could functional requirements. Every requirement has ID, source, priority, rationale, acceptance criterion and verification method (ISO/IEC/IEEE 29148).
Notes: Must is capped at roughly 60 percent of team capacity; anything implementing a safety requirement is Must regardless of effort.

## Slide 24: Functional requirements — data collection & processing
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-01 | Ingest river water levels at each station's interval | M | ≥ 99 % readings stored over 1 h [T]
FR-02 | Ingest observed / forecast rainfall from a public API | M | Hourly Open-Meteo data stored
FR-03 | Import boundaries, roads, shelters, population | M | Invalid geometry rejected
FR-04 | Ingest GloFAS discharge forecast (advisory) | C | Daily forecast tagged advisory
FR-05 | Scenario player replays scripted data (for testing) | M | Readings match script timing
FR-06 | Validate schema, unit and plausible range | M | Out-of-range → BAD, excluded
FR-07 | Detect missing data after the staleness window | M | Stale event ≤ 60 s [T]
FR-08 | Flag spikes, flatlines and impossible rates | M | Each fault flagged SUSPECT
FR-09 | Detect conflicts between linked sources | S | Conflict event on dashboard
FR-10 | Store source, raw payload, quality per reading | M | No null provenance fields
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 25: Functional requirements — risk assessment
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-11 | Compute a level for every Area Unit with rules R1–R10 | M | 100 % match scenario oracle [T]
FR-12 | Recompute affected areas within 60 s [T] | M | p95 ≤ 60 s over 100 runs
FR-13 | Show risk map with colour, pattern and label | M | Label on every area; a11y pass
FR-14 | Store inputs, rules fired and versions per result | M | Re-run reproduces the level
FR-15 | Assign HIGH / MEDIUM / LOW confidence | M | Stale gauge → LOW + badge
FR-16 | Rank WARNING+ areas by vulnerability index | S | Matches hand calculation
FR-17 | Use ML forecast as advice only, max WATCH | C | ML-only signal → ≤ WATCH
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 26: Functional requirements — warning management
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-18 | Create one proposal when a level reaches WATCH+ | M | 1 proposal ≤ 60 s [T]
FR-19 | Auto-publish WATCH if region policy allows | S | Audit shows actor = system
FR-20 | WARNING: 1 approver; CRITICAL: 2 distinct approvers | M | Same user twice is rejected
FR-21 | Escalate an undecided CRITICAL at timeout | S | Escalation + labelled publish
FR-22 | Let approvers edit message, areas, validity | M | Edit diff in audit log
FR-23 | Escalate as a new version superseding the old | M | v1 SUPERSEDED, one message
FR-24 | One-tap acknowledge: “I am safe” / “I need help” | S | Help request → incident
FR-25 | Require a reason to cancel; send all-clear to all | M | All-clear count = original
FR-26 | De-escalate only after the hold time (hysteresis) | M | ≤ 1 change per hold window
FR-27 | Expire at valid-until; remind before expiry | S | EXPIRED + reminder sent
FR-28 | One active warning per area; never below official | M | DB constraint blocks a 2nd
FR-29 | Render from templates with all mandatory fields | M | Linter rejects missing field
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 27: Functional requirements — citizen services
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-30 | Deliver to every subscription in the target areas | M | 100 % in-area, 0 outside [T]
FR-31 | Show level, action, confidence, last update | M | Card matches template
FR-32 | Subscribe to ≤ 5 areas, incl. proxy, no account | S | Phone-only subscription works
FR-33 | Level-specific instructions: what to take / not do | M | Reviewed by DRR proxy
FR-34 | Find area by list, consented GPS or QR code | S | Correct area for test points
FR-35 | SMS channel (gateway adapter), each language, ≤ 2 segments | M | Length test passes
FR-36 | Request assistance → incident for operators | S | On dashboard ≤ 10 s [T]
FR-37 | Report conditions: location, depth, photo, text | M | Appears with status “new”
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 28: Functional requirements — evacuation & shelters
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-38 | Nearest open shelters with capacity, by safe route | M | Full / closed never returned
FR-39 | Filter shelters: accessible, medical, livestock | S | Only matching shelters
FR-40 | Shelter details incl. occupancy timestamp | M | All fields displayed
FR-41 | Walking or vehicle route to the chosen shelter | M | Routes for 20 test pairs
FR-42 | Exclude hazard zones, closures, unsafe bridges | M | 0 routes cross exclusions
FR-43 | Operators add / remove road and bridge closures | M | New routes avoid closure
FR-44 | Alternative route, else “no safe route” + advice | M | Never returns an unsafe route
FR-45 | Push a re-route when a closure affects a route | S | Notice ≤ 60 s [T]
FR-46 | Show route warnings (near river, data incomplete) | S | Warning text shown
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 29: Functional requirements — offline & dashboard
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-47 | Offline cache: risk, warnings, shelters, numbers | M | Renders offline + timestamp
FR-48 | Status page: health and freshness per source | M | Degraded shown ≤ 60 s [T]
FR-49 | SMS fallback when push fails (WARNING+) | S | Both attempts recorded
FR-50 | Static snapshot every 60 s if backend is down | S | Snapshot ≤ 2 min old
FR-51 | Live map: risk, stations, warnings, shelters | M | Updates ≤ 5 s [T]
FR-52 | Area list by level, vulnerability and trend | M | Order verified
FR-53 | Manual warning with recipient preview | M | Preview = actual deliveries
FR-54 | Evacuation progress: acks, occupancy, requests | S | Updates with simulated acks
FR-55 | Shelter managers update status and occupancy | M | “Full” removed immediately
FR-56 | Triage reports: verify, reject, duplicate, incident | M | Transitions audited
FR-57 | Delivery statistics per warning and channel | M | Equal to database counts
FR-58 | Export active warnings as CAP 1.2 / JSON | C | Validates against CAP schema
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 30: Functional requirements — logging & administration
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-59 | Append-only audit of all critical actions | M | UPDATE / DELETE denied
FR-60 | Event timeline export (CSV / JSON) | S | All event types present
FR-61 | What-if replay with other config (sandbox) | C | Live data unaffected
FR-62 | Post-event metrics: lead time, FP, FN, delivery | S | Report per scenario
FR-63 | Configure regions and areas from files | M | 2nd municipality, no code
FR-64 | Versioned stations, links and thresholds | M | Old versions retrievable
FR-65 | Message templates with mandatory-field linting | M | Bad template not saved
FR-66 | Users, roles and geographic scopes | M | Ward 5 can't approve Ward 6
FR-67 | Toggle hazards, sources and region policies | M | Behaviour follows policy
FR-68 | Deployment Profile holds all country-specific settings | M | 2nd country profile, no code
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 31: Functional requirements — field devices & satellite data
ID | Requirement (the system shall …) | Pri | Acceptance criterion
FR-69 | Ingest gauge-node readings over MQTT / HTTPS, per-device keys | M | Pilot readings stored ≤ 60 s [T]
FR-70 | Register devices; watch heartbeat, battery, signal | M | Missed heartbeat alert ≤ 5 min [T]
FR-71 | Ingest satellite rainfall (NASA GPM IMERG) per catchment | M | Catchment totals stored each run
FR-72 | Ingest satellite flood extent (Sentinel-1) as hazard zones | S | Flood polygons feed routing
FR-73 | Ingest DHM station data via agreed feed | S | Adapter passes on sample data
FR-74 | Trigger sirens only from approved warnings; siren confirms | M | Command + ack logged ≤ 30 s [T]
FR-75 | Siren test / exercise mode and weekly silent self-test | S | Self-test logged weekly
NFR-HW1 | Gauge node runs without solar charge | S | ≥ 72 h [T]
NFR-HW2 | Store-and-forward buffer when network is down | M | ≥ 24 h of readings
NFR-HW3 | Weatherproof (IP65+), mounted above flood mark | S | Installation checklist
NFR-HW4 | Unique device credentials; signed firmware | M | Security test
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Full statements with source stakeholder, rationale and verification method are in REQUIREMENTS_ENGINEERING.md §4.

## Slide 32: Non-functional — performance & availability
ID | Requirement | Pri | Target / measurement
NFR-PF1 | Observation → warning proposal latency | M | ≤ 60 s p95 [T]
NFR-PF2 | Dispatch to 1,000 recipients; CRITICAL first | M | ≤ 60 s [T]
NFR-PF3 | Public API / route API response time | M | ≤ 1 s / ≤ 3 s p95 [T]
NFR-PF4 | Light citizen page on slow 3G | S | ≤ 300 KB, usable ≤ 5 s [T]
NFR-PF5 | Dashboard realtime update | M | ≤ 5 s [T]
NFR-A1 | Public endpoint availability over a 72-h test | S | ≥ 99 % [T]
NFR-A2 | Static fallback independent of backend | S | Kill test passes
NFR-A3 | Stateless backend, ≥ 2 instances, leader lock | C | No duplicate jobs
NFR-A4 | No deploys while any area is at WARNING+ | S | Deploy script refuses
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: Handset delivery depends on external networks and is measured, not guaranteed.

## Slide 33: Non-functional — reliability & usability
ID | Requirement | Pri | Target / measurement
NFR-R1 | Only validated data drives risk computation | M | Fault-injection tests
NFR-R2 | Isolate adapter failures (timeout, circuit breaker) | M | Other sources keep running
NFR-R3 | At-least-once delivery without duplicates | M | Crash mid-batch test
NFR-R4 | Recover and recompute after restart | M | ≤ 2 min [T]
NFR-R5 | Daily backups; restore rehearsed once | S | Drill record
NFR-U1 | One primary action per screen, plain language | M | ≥ 80 % correct in 30 s [T]
NFR-U2 | WCAG 2.2 AA on citizen pages | M | 0 critical axe issues
NFR-U3 | Level by word + icon + colour (+ sound) | M | Inspection
NFR-U4 | Every configured language complete; packs | M | Dummy pack renders
NFR-U5 | Read-aloud of the action card | S | Demonstration
NFR-U6 | Approve in ≤ 3 clicks with evidence visible | S | Task analysis
NFR-U7 | Citizen System Usability Scale score | S | SUS ≥ 68 [T]
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: SUS 68 is the commonly cited average score.

## Slide 34: Non-functional — scalability & interoperability
ID | Requirement | Pri
NFR-SC1 | New region by configuration only | M
NFR-SC2 | New hazard via plug-in, no core change | S
NFR-SC3 | New source = 1 adapter + 1 row | M
NFR-SC4 | Documented path to national scale | C
NFR-M1 | Modules talk via interfaces only | S
NFR-M2 | No hard-coded thresholds or strings | M
NFR-M3 | ≥ 80 % coverage on safety modules [T] | M
NFR-M4 | Schema changes via migrations only | M
NFR-M5 | Lint and format enforced in CI | S
ID | Requirement | Pri
NFR-I1 | CAP 1.2 export | C
NFR-I2 | GeoJSON exchange, WGS84 | M
NFR-I3 | Common channel adapter interface | M
NFR-I4 | Pull and push (webhook) ingestion | S
NFR-I5 | OSM attribution (ODbL) | M
NFR-L1 | UTF-8; Gregorian + local calendar option | S
NFR-L2 | Native numerals per language | C
NFR-L3 | Portable to any PostgreSQL + PostGIS | S
Priority (4-week MoSCoW): M Must · S Should · C Could [T] = semester acceptance target, not a real-world guarantee
Notes: These requirements make the system adaptive: new regions, hazards, sources and channels without redevelopment.

## Slide 35: Safety requirements
ID | Safety requirement (all Must) | Mitigates
SR-01 | No warning silently dropped; failed deliveries shown to operators | F10, F11
SR-02 | ≥ 1 approver for WARNING, ≥ 2 distinct approvers for CRITICAL | F16, F17
SR-03 | Routes never cross hazard zones, closures or unsafe bridges | F12
SR-04 | Every route and shelter shows its data time and limitations | F12, F14
SR-05 | Never recommend shelters that are full, closed or in a hazard zone | F13
SR-06 | Missing or bad data never lowers a risk level by itself | F4–F6
SR-07 | Never publish below an official warning; always name the issuer | F7
SR-08 | Confidence shown everywhere; LOW-confidence CRITICAL highlighted | F6, F8
SR-09 | Corrections reach every original recipient on the same channels | F17
SR-10 | Every screen: decision support; officials on site take precedence | F18
SR-11 | Forecast-only or ML-only signal cannot exceed WATCH | F8, F19
SR-12 | Exercise mode prefixes “EXERCISE”; simulated data blocked in live | F16, F17
SR-13 | No siren sounds without authorized approval; commands signed | F16, F17
SR-14 | Devices fail safe: offline siren keeps manual trigger; gauges buffer | F2, F5
Higher verification rigour: each SR has a unit / property test and an end-to-end scenario test; changes need two reviewers, one of them the project lead.
Notes: Derived from the 20 failure scenarios (F1–F20). These are the non-negotiable core of the system.

## Slide 36: Security and privacy requirements
Security | Requirement
SEC-01 | MFA (TOTP) for operators and admins
SEC-02 | Authorization in API and database RLS
SEC-03 | TLS 1.2+; secrets never in Git
SEC-04 | Separate admin and operator roles
SEC-05 | No unauthenticated warning actions
SEC-06 | Rate-limited, unverified reports never trigger
SEC-07 | Login throttling
SEC-08 | Dependency scanning in CI
SEC-09 | Input validation, XSS encoding, safe uploads
SEC-10 | Unique device keys; signed firmware updates
Privacy | Requirement
PRV-01 | Store only area, language, endpoint, consent
PRV-02 | Location used transiently unless opted in
PRV-03 | Phone numbers encrypted, hashed lookup
PRV-04 | Disability data voluntary, scoped, deletable
PRV-05 | Retention: reports 90 days, subs 12 months
PRV-06 | Notice in every language; one-step unsubscribe
PRV-07 | No third-party trackers
PRV-08 | EXIF stripped from report photos
Basis: OWASP ASVS subset, each country's data-protection law (pilot: Nepal), privacy-by-design. SEC-01, PRV-03, -05, -08 Should; rest Must.
Notes: Misuse case driving SEC-05: an attacker or careless admin creating a false evacuation warning.

## Slide 37: Use cases: 13 specified in full
Citizen
UC-01 Receive flood warning
UC-02 Check local risk level
UC-03 Request evacuation guidance
UC-04 Find nearest shelter
UC-05 Report flooding
Authority
UC-06 Monitor flood risk
UC-07 Issue emergency warning
UC-08 Update shelter availability
System
UC-09 Detect abnormal data
UC-10 Generate risk assessment
UC-11 Handle unavailable data
UC-12 Handle conflicting data
Administrator
UC-13 Configure a region
Each use case: actor · preconditions · trigger · main flow · alternative flows · exception flows · postconditions · related requirements (docs/05).
Notes: Includes: UC-03 includes UC-04; UC-10 includes UC-09.

## Slide 38: UC-07 Authority issues an emergency warning
Actor
Operator (initiator), approver(s)
Precondition
MFA session; scope covers areas
Trigger
Proposal, or local knowledge of danger
Main flow
1
Select areas, level, template
2
Message filled in every configured language
3
Preview recipients, contradiction check
4
Submit → PROPOSED
5
Approver(s) review evidence
6
ACTIVE → delivery (UC-01)
7
Track delivery and acks
Alternative flows
A1 Escalate existing warning → new version
A2 Cancel → reason + all-clear to same people
A3 Self-approval for WARNING only if policy allows
Exception flows
E1 Contradiction → blocked with explanation
E2 Second approver absent → timeout escalation
E3 Rejected → reason recorded · E4 Exercise → prefix
Related requirements: FR-20–FR-23, FR-25, FR-28, FR-29, FR-53, SR-02, SR-07, SR-09, SR-12, SEC-01, SEC-05
Notes: Postcondition: warning ACTIVE or REJECTED with full audit trail.

## Slide 39: UC-11 System handles unavailable data
Actor
System (health monitor); operators
Precondition
Staleness windows configured
Trigger
No valid data within the window
Main flow
1
Mark source stale; open quality event
2
Hold last level; confidence LOW
3
Use upstream and rainfall inputs
4
Alert operators and admin
5
Citizens see “data delayed”
6
On recovery: close event, recompute
Alternative flows
A1 Area was NORMAL, no other signal → UNKNOWN for operators
A2 Long outage in monsoon → request manual gauge readings
Exception flows
E1 All sources down → system-wide banner and manual procedures
Related requirements: FR-07, FR-15, FR-48, SR-06, NFR-R2 — scenario test ST-04
Notes: Silence is never interpreted as safety: this is the core fail-safe rule SR-06.

## Slide 40: User stories (24 total — examples)
ID | User story | Req
US-01 | As a riverside resident, I want a warning in my language when my ward is at risk, so I can move my family early | FR-30
US-02 | As a feature-phone user, I want warnings by SMS, so I get them without internet | FR-35
US-03 | As a son working abroad, I want to subscribe to my father's ward, so I can call him | FR-32
US-06 | As a wheelchair user, I want accessible shelters and step-free routes, so I can reach safety | FR-39
US-10 | As a ward focal person, I want a proposal with evidence, so I approve quickly but responsibly | FR-18, 20
US-12 | As an operator, I want to cancel a wrong warning and correct the same people | FR-25
US-16 | As an admin, I want to know when a gauge goes silent, so silence isn't read as safety | FR-07
US-21 | As the national hydromet authority, I want the system never to contradict our warning | FR-28
Key stories carry Gherkin acceptance tests, e.g. “Given a gauge stops while Ward 3 is at WARNING, then Ward 3 stays at WARNING with LOW confidence”.
Notes: All 24 stories in docs/05.

## Slide 41: Failure scenarios F1–F10
# | Scenario | Sev | Prob | Key mitigation | Requirements
F1 | Internet fails | 3 | H | PWA offline cache, SMS, static CDN page | FR-47, FR-50
F2 | Mobile network fails | 4 | M | Early WATCH, sirens, volunteers, re-send | SR-01, FR-57
F3 | Electricity fails | 3 | H | Cloud hosting, low-power app, charge advice | NFR-A2
F4 | Weather API down | 2 | M | Circuit breaker, cached forecast, hold level | NFR-R2
F5 | River data unavailable | 4 | M | Hold level, LOW confidence, manual readings | FR-07, SR-06
F6 | Incorrect data | 4 | M | Range / spike checks, human approval | FR-06, FR-08
F7 | Conflicting sources | 3 | M | Conservative level, operator resolves | FR-09, SR-07
F8 | False flood prediction | 3 | H | Tiered levels, approval, hysteresis | FR-26, SR-08
F9 | Flood not detected | 4 | M | Upstream + rain rules, reports, manual alert | FR-37, FR-53
F10 | Warning delayed | 4 | M | Auto WATCH, timeout escalation, priority | FR-21
Severity 4 catastrophic … 1 minor · Probability H / M / L per monsoon season — qualitative estimates [A]; detection, recovery, owner in docs/06
Notes: FMEA-style analysis; every safety requirement traces to at least one scenario.

## Slide 42: Failure scenarios F11–F20
# | Scenario | Sev | Prob | Key mitigation | Requirements
F11 | Warning not delivered | 4 | M | Retries, SMS fallback, undelivered stats | SR-01, FR-49
F12 | Route blocked | 4 | M | Hazard-aware routing, alternative, re-route | SR-03, FR-45
F13 | Shelter unavailable | 3 | M | Live status, exclude unsafe, alternative | SR-05, FR-55
F14 | GPS inaccurate | 3 | M | Confirm on map if accuracy > 100 m | FR-34
F15 | Server crash in emergency | 4 | L | Restart + recompute ≤ 2 min, static fallback | NFR-R4
F16 | Cyberattack: fake warning | 4 | L | MFA, RLS, two-person rule, rate limits | SR-02, SEC-05
F17 | Admin issues wrong warning | 3 | M | Preview, 2nd approver, cancel + correction | FR-25, SR-09
F18 | Levels misunderstood | 3 | H | Action-first text, icons, local languages, testing | FR-29, NFR-U1
F19 | Warning fatigue | 4 | M | Notify on change, hysteresis, tuning | FR-26, FR-62
F20 | No coverage in mountains | 4 | H | Coverage flags, community EWS, sirens | FR-16, NFR-I3
Severity 4 catastrophic … 1 minor · Probability H / M / L per monsoon season — qualitative estimates [A]; detection, recovery, owner in docs/06
Notes: FMEA-style analysis; every safety requirement traces to at least one scenario.

## Slide 43: Risk matrix and residual risk
Low
Medium
High
Sev 4
F15, F16
F2, F5, F6, F9, F10, F11, F12, F19
F20
Sev 3
—
F7, F13, F14, F17
F1, F3, F8, F18
Sev 2
—
F4
—
Probability →
Residual risk
Mitigation moves most scenarios to ALARP (as low as reasonably practicable).
F9 (fast flash floods) and F20 (no coverage) cannot be made acceptable by software alone.
Key RE finding: some safety goals must be assigned to human and organisational agents — community warning systems, volunteers, sirens, radio — and the limitation is stated openly (SR-10).
Notes: Fault tree for the top event 'person not warned in time' is in docs/06 §1.2.

## Slide 44: Conflicting requirements and how RE resolves them
Conflict | Resolution in the requirements | RE technique
C1 Early warning vs false alarms | Tiered levels; stronger evidence + approval higher up | Goal / obstacle analysis
C2 Automation vs human authority | Graduated autonomy + timeout escalation | Trade-off workshop, ADR
C3 Privacy vs location tracking | Area subscriptions; consented location only | Privacy impact assessment
C4 Accuracy vs speed | Bounded validation; LOW confidence, not waiting | Quantified NFRs
C5 Rich data vs simple UI | Role-based views, progressive disclosure | Personas, prototyping
C6 Central vs local authority | Official warning sets a floor; local may add | Viewpoints, RACI
C7 Coverage vs infrastructure | Channel-agnostic core, SMS, volunteers | Responsibility assignment
C8 Frequent alerts vs fatigue | Notify on change only; CRITICAL unmutable | Scenario simulation
Process: detect (conflict matrix, viewpoints) → analyse (data / interest / value / authority) → negotiate (WinWin with scenarios) → decide and record (ADR) → make configurable where context-dependent → validate.
Notes: Three more conflicts (open data vs security, volunteer reports vs sensors, features vs timeline) in docs/06 §2.

## Slide 45: Global by design: core vs configurable requirements
Core — never configurable
Data validation and staleness detection
Data loss never lowers risk
One active warning; no contradiction
Human approval for the highest level
Corrections to the same recipients
Safe routing and shelter filters
Audit log
Security and privacy baselines
Disclaimer and exercise labelling
Configurable — per deployment
Country Deployment Profile and admin hierarchy
Area granularity (ward or river reach)
Hazards and thresholds
Languages
Channels and fallbacks
Approval tiers, timeouts, auto-publish
Poll intervals and retention periods
Routing defaults, emergency numbers
Rural vs urban shelter types
Principle [D]: safety invariants are fixed; context is configuration — validated, versioned, two-person approved and testable by replay.
Notes: This lets the same system serve a rural Terai municipality, Kathmandu, or another country without weakening safety.

## Slide 46: Requirements engineering lifecycle applied
1
Elicitation
Interviews, questionnaire, focus groups
2
Stakeholder analysis
Onion model, power / interest
3
Analysis & modelling
Goals, use cases, misuse cases
4
Classification
FR / NFR (ISO 25010), core vs config
5
Prioritization
Weighted MoSCoW
6
Conflict resolution
Conflict matrix, WinWin, ADRs
7
Specification
IEEE 29148, EARS, Gherkin
8
Validation
Walkthroughs, prototypes, usability
9
Verification
Requirement-tagged tests
10
Requirements mgmt
Git baselines, RTM in CI
11
Change mgmt
Change requests, CCB
Iterative: weekly baselines (v1.0 week 1 → v1.1 week 2 → v2.0 week 4); volatile items (thresholds, policies, languages) are configuration, so change rarely needs redesign.
Notes: Ambiguity log resolves vague terms: 'timely' → ≤ 60 s [T]; 'nearby' → safe-route distance; 'safe route' → excludes WARNING+ zones, closures, unsafe bridges.

## Slide 47: 4-week delivery plan
Week 1
Foundations
Schema, RLS, live satellite + weather adapters, order hardware, i18n UI; baseline signed
Week 2
Core pipeline
Live data → risk → approval → delivery; gauge node sending data; validation round 1
Week 3
All Must items
Siren pilot (test mode), device monitoring, routing, dashboard; install gauge with local permission
Week 4
Polish & prove
Field test, usability tests, traceability check, report, demo; feature freeze day 3
51
Must FRs
20
Should FRs
4
Could FRs
Not this semester: own country-wide sensors, autonomous sirens, cell broadcast, public alerts before government sign-off, full landslide and earthquake models — see roadmap.
Notes: Rule: all Must items done by end of week 3; week 4 is Should items, validation, report and demo.

## Slide 48: Roadmap from semester MVP to government launch
Phase 0
Semester MVP
4 weeks
Live satellite + weather data · 1–3 own gauges · siren pilot in test mode · full warning workflow · exercise mode only
Phase 1
Partnership
≈ 1–3 months [A]
Meet DHM, NDRRMA and a pilot municipality · data-sharing MoU · DHM feed live · security review · real SMS gateway
Phase 2
Shadow pilot
one monsoon [A]
Runs alongside the official process with no public alerts · compare lead time and false alarms · train operators
Phase 3
Government launch
after sign-off
Authorities own operation · government hosting · sirens and cell broadcast live · district by district, then national
Each phase gate needs the agreement of the responsible authority. Shadow mode means the system runs for real but nobody is alerted by it until the government approves going live. Durations are planning assumptions [A].
Notes: The semester delivers Phase 0. The team continues Phases 1-3 after the semester.

## Slide 49: Traceability: stakeholder to test
Requirement | Need | Goal | Use case | Component | Test
SR-01 / FR-30 | STK-01, 09 | G3.1 | UC-01 | Notification dispatcher | ST-08
SR-02 / FR-20 | STK-07, 12 | G3.2 | UC-07 | Warning manager + RLS | UT-20, ST-12
SR-03 / FR-42 | STK-04 | G4 | UC-03 | Evacuation router | PT-42, ST-10
SR-05 / FR-38 | STK-04 | G4 | UC-04 | Shelter module | UT-38, ST-09
SR-06 / FR-07 | STK-15 | G6 | UC-11 | Validation + risk engine | ST-04
SR-07 / FR-28 | STK-08 | G3.1 | UC-07 | Warning manager + DB index | UT-28
SR-09 / FR-25 | STK-07 | G3.1 | UC-07 | Warning manager + dispatcher | ST-14
SR-12 | STK-12 | G7 | UC-07 | Warning manager | ST-13
Checked in CI: every Must FR → need, use case, component, test · every SR → failure scenario + unit test + scenario test · no orphan tests · tests tagged @pytest.mark.req("FR-42")
Notes: Full matrix for all critical requirements in docs/08 §3.

## Slide 50: Verification, validation and evaluation
Verification — built right?
Unit and property tests (pytest, hypothesis)
14 scripted scenario tests ST-01 – ST-14
RLS tests with role-specific JWTs
End-to-end UI tests (Playwright)
Load tests (k6) · security scans (ZAP, gitleaks)
Validation — right system?
Requirements walkthrough (week 1)
Prototype demo to proxies (week 2)
Usability + comprehension tests (week 4)
ISO 29148 quality checklist
Evaluation metric | Target [T]
Warning generation latency | ≤ 60 s p95
Dispatch to 1,000 recipients | ≤ 60 s
Classification vs scenario oracle | 100 %
False negatives in safety scenarios | 0
Unsafe routes / shelters recommended | 0
Availability over 72 h | ≥ 99 %
SUS score / task success | ≥ 68 / ≥ 80 %
Critical accessibility issues | 0
Must requirements traced | 100 %
Targets are prototype acceptance targets in a simulated setting — no claim about real-world hydrological accuracy.
Notes: False-positive rate is reported and reviewed but not hard-capped (conflict C1).

## Slide 51: Ethical and social considerations
False alarms
Tiered levels, human approval, published reviews
Missed warnings
Conservative rules; “no warning ≠ safe” stated
Responsibility
Mandated authority approves; full audit trail
Privacy & surveillance
Minimal data, purpose limit, no tracking
Digital exclusion
SMS, proxies, volunteers, sirens
Language & accessibility
Language packs, icons, audio, WCAG 2.2 AA
Algorithmic bias
Coverage and confidence shown per area
Human oversight & trust
Evidence at approval; one official voice
The system provides warnings and decision support — not guaranteed predictions and not guaranteed safety. Research with people affected by disasters needs ethics approval and informed consent.
Notes: Full analysis in docs/09 §2.

## Slide 52: Limitations and future extensions
Limitations
Not yet authorized for public warnings
Few own sensors; national coverage needs DHM data
Satellite rainfall arrives hours late, coarse grid
Thresholds must be agreed with national agencies
Many validations use proxy stakeholders
Rural OSM road data may be incomplete
Whether people act on warnings is not evaluated
Only one country profile piloted so far
Future extensions
Phase 1–3 roadmap to government launch
Landslide module via the HazardModel plug-in
GLOF monitoring with lake sensors
Cell broadcast, IVR, community radio
National authority feeds via CAP (pilot: DHM, BIPAD)
Second-country pilot with a new Deployment Profile
Advisory hydrological / ML forecasting (bounded by SR-11)
Notes: Stating limitations openly is part of the honesty requirement in the quality checklist.

## Slide 53: Conclusion
Requirements, not prediction
Flood warning framed as engineering requirements under uncertainty, traced from stakeholder to test.
Safety by design
Data loss never lowers risk, humans approve high-impact warnings, routes never cross known hazards.
Conflicts made explicit
Graduated autonomy, nested authority, tiered levels and privacy-by-design resolve real trade-offs.
Global yet safe
Fixed safety invariants; countries, hazards, languages and channels are configuration — Nepal is the first pilot.
AMHEWS complements national and local authorities (pilot: DHM, NDRRMA) — it does not replace them, and it does not guarantee prediction or safety.
Notes: Close by restating the core research question and how the requirements answer it in a testable way. Next step: build the 4-week prototype on Supabase, FastAPI and Next.js.